## Slide 1
Vehicle Detection and Monitoring using Magnetic Field Sensors
Pradeep Kumar. N (1BG10EC058)
Nikunj. T (1BG10EC054)
Nafeeya Samar (1BG10EC047)
Noor Zahara (1BG10EC055)
Project Guide:
Anuradha V. Rao

## Slide 2
Motivation:
Alleviation of traffic congestion by improving the efficiency of the current transportation system.
Solution: Real-time traffic surveillance
Requirement: Acquisition of traffic metrics (speed, volume etc.) which can be obtained using Magnetic sensors and Induction loops.
Objectives:
Development of traffic monitoring system using low power, low cost magnetic sensors and induction loops.
The data acquired is used to increase the efficiency and to enhance the capacity of the existing roadways.
Vehicle Detection and Monitoring using Magnetic Field Sensors

## Slide 3
Generic block diagram
Signal Processing System
Sensors
(A or B)
GUI
Monitoring System
Database
A: Induction loop
B: AMR sensor
Vehicle Movement
Vehicle Detection and Monitoring using Magnetic Field Sensors

## Slide 4
Block Diagram of Induction Loop Detector
Comparator
Change in Inductance of the loop
Microcontroller
(ATmega2560)
Frequency Counter
Vref
Colpitt’s Oscillator
GUI
Computer
Database
Change in magnetic field
Presence of Vehicle
Vehicle Detection and Monitoring using Magnetic Field Sensors

## Slide 5
Increment count and store
(max count: 232)
UART send: Vehicle detected
Measure frequency of comparator output
Flowchart for Induction Loop system
Wait for vehicle to move over the loop
Start
Yes
No
Frequency change > threshold?
L = L-ΔL; f = f+Δf
Vehicle Detection and Monitoring using Magnetic Field Sensors

## Slide 6
Circuit Diagram of Colpitt’s Oscillator and comparator
To μC
Vehicle Detection and Monitoring using Magnetic Field Sensors

## Slide 7
Typical oscillator and comparator output
Vehicle Detection and Monitoring using Magnetic Field Sensors

## Slide 8
Technical Specifications of Induction Loop detector
Induction Loop
    #12 AWG wire
    6 ft x 6 ft square loop
    Length of lead-in cable = 2m
    Inductance: 100µH
    MC33274 Quad Op-Amp IC used to build oscillator (50KHz) and comparator (Vcc = 5V)
    Microcontroller: ATmega2560 Arduino Board
        8-Bit, AVR enhanced RISC architecture
        256KBytes of In-System Self-Programmable Flash
        4Kbytes EEPROM
        8Kbytes Internal SRAM
Vehicle Detection and Monitoring using Magnetic Field Sensors

## Slide 9
Block Diagram of AMR sensor Vehicle Detection System
Transceiver
AMR sensor
Slave Module 2
Microcontroller
(Jennic)
Transceiver
GUI
Transceiver
AMR sensor
Slave Module 1
Microcontroller
(Jennic)
Microcontroller
(Jennic)
Computer
Database
Master Module
Vehicle Detection and Monitoring using Magnetic Field Sensors

## Slide 10
Start
Sensor output converted to digital value by ADC
Radio Transmission: Vehicle detected
Is ADC value > detection threshold?
Read ADC output
Flowchart for Slave Module
Yes
No
Calibrate Sensor
Vehicle Detection and Monitoring using Magnetic Field Sensors

## Slide 11
Start
Calculate speed = dist/(t2 – t1)
UART send: Vehicle detected
Radio packet pair Received?
Flowchart for Master Module
No
Increment count and store
(max count: 232)
Wait for Radio packet arrival from slaves 1 & 2
Yes
Vehicle Detection and Monitoring using Magnetic Field Sensors

## Slide 12
Technical Specifications of AMR sensor Vehicle Detection System
AMR sensor
  Supply voltage: 3 - 5V
  Sensitivity: 16 (mV/V)/(kA/m)
  Total power dissipation: 130mW
    Microcontroller: Jennic JN5148-001
      Low power 32-bit RISC CPU, 4 to 32MHz clock speed
  128kB ROM & 128kB RAM for boot loaded program code & data
  4-input 12-bit ADC, 2 12-bit DACs, 2 comparators
  2 UARTs
Vehicle Detection and Monitoring using Magnetic Field Sensors

## Slide 13
Technical Specifications of AMR sensor Vehicle Detection System
Radio Transceiver
  2.4GHz IEEE802.15.4 compliant
  Typical data rate: 256kbps
  500 & 667kbps High data rate modes
  Receiver sensitivity -95dBm
  Transmit power 2.5dBm
Vehicle Detection and Monitoring using Magnetic Field Sensors

## Slide 14
Snapshot of GUI for Induction Loop detector
Vehicle Detection and Monitoring using Magnetic Field Sensors

## Slide 15
Results for Induction Loop Detector
Dimensions | No. of turns | Center Frequency | Frequency drift
1.5ft x 1.5ft | 10 | 48.3 kHz | 500 Hz
6ft x 6ft | 2 | 80 kHz (Unstable) | Unreliable
6ft x 6ft | 3 | 51 kHz | 100 Hz
6ft x 6ft | 4 | 41 kHz | 30 Hz
Vehicle Detection and Monitoring using Magnetic Field Sensors

## Slide 16
Typical AMR sensor output
Vehicle Detection and Monitoring using Magnetic Field Sensors

## Slide 17
Snapshot of GUI for AMR sensor Vehicle Detection System
Vehicle Detection and Monitoring using Magnetic Field Sensors

## Slide 18
Proposed database format
Date | Vehicle count | Avg speed
Vehicle Detection and Monitoring using Magnetic Field Sensors

## Slide 19
Completed tasks
Induction loop detector
Building and testing the circuit
Program for frequency measurement and vehicle count
  AMR sensor Vehicle Detection System
Program for:
  Time synchronization of the slave modules
  Vehicle detection based on slope change
  Speed calculation based on difference in times between packets from the two slaves
Vehicle Detection and Monitoring using Magnetic Field Sensors

## Slide 20
Remaining tasks
Induction loop detector
Field tests to determine optimal area and no. of turns of the loop
Refining the program to reduce the probability of false counts
  AMR sensor Vehicle Detection System
Refining the program to reduce the probability of false counts
Finding a solution for the problem of sensor output saturation
Field tests to determine the optimal sampling freq for the sensor
Vehicle Detection and Monitoring using Magnetic Field Sensors

## Slide 21
References
[1] Ravneet Bajwa, Ram Rajagopal, Pravin Varaiya and Robert Kavaler. In-Pavement Wireless Sensor Network for Vehicle Classification.
[2] Sing Yiu Cheung, Sinem Coleri Ergen and Pravin Varaiya. Traffic Surveillance with Wireless Magnetic Sensors.
[3] Farshad Ahdi, Mehdi Kalantari Khandani, Masoud Hamedi, Ali Haghani.
Traffic data collection and anonymous vehicle detection using wireless sensor networks.
[4] Traffic Detector Handbook: Third Edition—Volume I. Publication No. FHWA-HRT-06-108.
Vehicle Detection and Monitoring using Magnetic Field Sensors